## Slide 1: E&LS Storage Track Final Presentation
Alex Christmas Brendan Gardner Max Maloney Jack Seilsopour

## Slide 2: Outline
Introduction
Rail Design
Lighting & Drainage Design
Construction Estimates
Conclusion
Questions

## Slide 3
Introduction
Max Maloney

## Slide 4: Project Introduction
Escanaba & Lake Superior Railroad
Contract Repair Shop
Existing Site
Railcars need to be stored/staged before shopping
Max Maloney

## Slide 5: Site Visit & Survey
Site Visit in January
Horizontal Survey
  Existing track
  Turnouts
Generally ﬂat site
Existing track not of high standard
Max Maloney

## Slide 6: Existing Conditions
E&LS boundary - blue
Existing track - orange
Car shop - pink
Oddly shaped site
Mainline parallel to southern property boundary
Max Maloney

## Slide 7: Existing Conditions - Track Capacity
Trk | Length | Cars | Notes
L3 | 883’ | 16 | Staging only
L2 | 930’ | 16 | Staging only
L1 | 985’ | 17 | Staging only
3 | 1063’ | 19 | Access to storage building
4 | 728’ | 13 | Access to 2nd building
5 | 573’ | 10 | Access to 2nd building
6 | 568’ | 10 | Access to 2nd building
Current Capacity: 68 railcars of dedicated space Expansion Goal: add 85 railcars of dedicated space
Max Maloney

## Slide 8: Design Standards
CN Industrial Track Standards
AAR Plate H clearance
envelope
Existing 15.5 and 17-degree curves into car shop
Several curved turnouts
Max Maloney

## Slide 9
Track Design
Alex Christmas

## Slide 10: Conceptual Design
Three areas identiﬁed for new track construction
  Two alternatives each
1 Whole-Site
Clean-Sheet Design

## Slide 11: Conceptual Design - Phases 1, 2 & 3

## Slide 12: Conceptual Design - Phase 4

## Slide 13: Final Design
Phase 1:
  A1-A2: 66 cars of new storage
Phase 2:
  L11: 10-18 cars as a run around
  L10-L4: 57 cars of new storage
Phase 3:
  3A-3B: 26 cars of new storage
New Storage Goal: 85 cars
New Storage Total: 146 cars
Site Total: 214 cars (up 215%)

## Slide 14: Final Design
Existing Track: ballast lift up to CN standards

## Slide 15
Lighting & Drainage Design
Brendan Gardner

## Slide 16: Exterior Lighting Design
US DOE Illumination Recommendations:
  0.2 fc min
  0.5 fc for security
Brendan Gardner

## Slide 17: Exterior Lighting Design
US DOE Illumination Recommendations:
  0.2 fc min
  0.5 fc for security
80’ Spacing w/ 40’ poles
Brendan Gardner

## Slide 18: Exterior Lighting Layout Plan
53 poles, 2 ﬁxtures each
CN requires 13.5’ object clearance
  Round up to 15’
on-center spacing to account for pole foundations
Keeps aisleways open for vehicles and snow removal
Brendan Gardner

## Slide 19: Exterior Lighting Design
Lithonia Lighting model R5
90° cone of useful light
Diagrams at right show lighting areas for diﬀerent AAR clearance envelopes
  Full illumination in aisles
  Shadows occur between track pairs when occupied
Plate H
Brendan Gardner
Plate C

## Slide 20: Drainage Design
471,800 SF drainage area
Sandy underlying soils
100-year, 24-hour storm: 5” of precipitation
Runoﬀ:
  2.54” for avg soil moisture
  4.11” for high soil moisture
Brendan Gardner

## Slide 21: Drainage Design
Underground Detention Basin
  HDPE perforated pipe
HDPE feeder lines
Ductile Iron Pipe under track
Brendan Gardner

## Slide 22: Drainage Design
4’ HDPE perforated pipe
5’ pipe centers
Underground Basin
  High soil moisture: 12890’
  Avg soil moisture: 7960’
Brendan Gardner

## Slide 23: Drainage Design
4’ HDPE perforated pipe
5’ pipe centers
Underground Basin
  High soil moisture: 12890’
  Avg soil moisture: 7960’
Brendan Gardner

## Slide 24: Drainage Further Considerations
Soil Testing
  Water Table & Inﬁltration
Runoﬀ assumptions
  High v Avg soil moisture?
Bottomless catch basins
  Higher inﬁltration?
Outlet?
May be acceptable as-is
Brendan Gardner

## Slide 25
Estimating
Jack Seilsopour

## Slide 26: Estimate Assumptions
Track Materials
  All-New
    Direct from manufacturer
  Relay Condition
    Previous use elsewhere, purchased by E&LS
  On-Hand
    Previous use elsewhere, already owned by E&LS
Lighting and Drainage
  All-New

## Slide 27: Estimate Assumptions
Equipment
  Rental Rates
Labor
  MDOT Prevailing Wage
  RS Means Crews
Sources:
  RS Means
  Heavy Rail Suppliers

## Slide 28: Construction Estimates
Phase One - 4,032’
  Total - $1.6M
  Duration ~ 65 Days

## Slide 29: Construction Estimates
Phase Two - 4,376’
  Total - $2.1M
  Duration ~ 60 Days

## Slide 30: Construction Estimates
Phase Three - 1,660’
  Total - $824K
  Duration ~ 40 Days

## Slide 31: Construction Estimates
Lighting and Drainage
  Total - $2.1M
  Duration ~ 52 Days
Existing Track Raise
  Total - $2.9M
  Duration ~35 Days

## Slide 32: Construction Estimates
Construction Estimate Summary
  Total Cost - $9.5M
  Total Duration ~ 252 Days
Relay material can lower price by $1.2M
On-Hand material can lower price by $2.0M

## Slide 33: Acknowledgements
Mike Logan - Client
Daniel Block - Client
Jason Campbell - Client
Dave Nelson - Advisor
Terry Flower - City of Escanaba
Jim Sharpe - Sharpe Engineering
Joseph Foster - MTU Surveying Instructor

## Slide 34: Questions?
Alex Christmas Brendan Gardner Max Maloney Jack Seilsopour

## Slide 35: Questions?